## Slide 1: Pulmonary Embolism Detection
13/11/2020

## Slide 2: Introduction

## Slide 3: Pulmonary Embolism (PE)
A PE is a blood clot in the vessels of the lungs that can potentially be life-threatening.
They are primarily diagnosed using CT-Scans.
CT-Scan of healthy lungs
CT-Scan of lungs with PE

## Slide 4: CT Scans
CT scans measure the radiation absorption coefficient of an area
  Normalized to be in Hounsfied Units
  Values tend to range from -1000 to 3000
Radiologists use windowing to visualize CT scans.
  Windows are characterized by their width WW and level WL.
  Values are clipped to be in [WL – WW/2 ; WL + WW/2] and then rescaled
  Different types of tissues are better evaluated using different windows.

## Slide 5: Windows
Lung window
Level = -600
Width = 1500
PE window
Level = 100
Width = 700
Mediastinal window
Level = 40
Width = 400

## Slide 6: Target & Metric
Targets :
Image level :
  PE Present on image
Patient level :
  Exam :
    Negative for PE or Indeterminate
  Location of the PE :
    Central PE or Left PE or Right PE
  Ventricle Ratio :
    RV/LV Ratio >= 1 or RV/LV Ratio < 1
  PE Characterization :
    Chronic or Acute & Chronic
Metric :
Image level :
  Weighted log loss over all the targets
  Weights defined by specialists
  Additional constraints on predictions
Patient level :
  Weighted log loss
  Weight is proportional to the number of positive images
  Images with no positives have weight 0

## Slide 7: Validation – 5-fold example
There are 7300 patients in the training set
1
2
3
4
5
7300 patients
Val
Val
Val
Val
Val
The data is split in 5
Each of the 5 subsets is used for validating while the rest is used for training
Fold 1
Fold 2
Fold 3
Fold 4
Fold 5
At each fold, the predictions are stored, and in the end you can evaluate your model on the whole dataset
7300 predictions

## Slide 8: Solution Overview

## Slide 9
Dicom
File
Convolutional Neural Network
PE Classifier
Features
1st Level Model
2nd Level Model
Feature extraction
Sequential Model
Image level prediction
Image level predictions
Patient level predictions
Classifier
Classifier
Pooling

## Slide 10: 1st Level Model

## Slide 11: Overview
The first level model is a pretrained Convolutional Neural Network that will be finetuned on our data and used for feature extraction
There exists numerous architectures in the literature :
  ResNets, ResNeXts, EfficientNets, SENets, DenseNets, …
  Most architectures exist in different sizes
    ResNet-34, ResNet-50, ResNeXt-50, ResNeXt-101, EfficientNet-b0, EfficientNet-b1, …
Build a robust pipeline and train some models :
  I started with a ResNeXt-50, rapidly tried a ResNeXt-101, and finally used an EfficientNet-b3 which performed best

## Slide 12
Dicom
File
Windowing
EfficientNet-b3
Dense Layer
Features
1536
Image level prediction
Sampling,
Augmentations
1
256 x 256
Windowing :
Described earlier
Pre-computed jpegs by Ian Pan
Sampling :
Use only 30 slices per scan instead of the 400+ available
Speeds-up training :
  A model takes ~9 hours / fold to train for 20 epochs
Augmentations :
Flipping
Shifting, Scaling, Rotating
Brightness , Gamma and Contrast adjustments
Distortions

## Slide 13: 2nd Level Model

## Slide 14
Image level predictions
Patient level predictions
Dense
Pooling
Multi-Layer
Perceptron
Bidirectional LSTM
2D Features
1536 x n
512 x n
512
Dense
n
9
Multi-Layer Perceptron :
2x Dense + ReLU
Adds more information to the features
Bidirectional LSTM :
Propagates information between adjacent features
Pooling :
Simple averaging over the last axis
1700 training samples, extracted using the pretrained model.

## Slide 15: Results
Validation score : 0,175
Public Leaderboard score : 0,182 (20th)
Private Leaderboard score : 0,178 (18th)

## Slide 16: Going further

## Slide 17: Improving the results
With more time & computational resources …
  Use bigger images
  Use bigger CNNs
Winning ideas
  Only use the PE window, use the neighbors to get a 3-channel image
  Add a lung localization model
  Use separated models for the patient targets
  CT-Scans lengths vary a lot, padding is not optimal

## Slide 18
Dicom
File
Convolutional Neural Network
BCC Classifier
Features
1st Level Model
2nd Level Model
Feature extraction
Sequential Model
Image level prediction
Image level predictions
Patient level predictions
Classifier
Classifier
Pooling
Issues :
We don’t have image level labels
We have way fewer patients

## Slide 19: Links
Competition :
  https://www.kaggle.com/c/rsna-str-pulmonary-embolism-detection
Code :
  https://github.com/TheoViel/kaggle_pulmonary_embolism_detection
1st place solution :
  https://www.kaggle.com/c/rsna-str-pulmonary-embolism-detection/discussion/194145
2nd place solution :
  https://www.kaggle.com/c/rsna-str-pulmonary-embolism-detection/discussion/193401